## Slide 1: Basics of Mobile Robotics
Playing around with a Thymio Robot

## Slide 2: The Map
Notes: JB 20 sec
Describe the function of the different objects

## Slide 3: Vision
Notes: Antoine 40 sec
Describe the different steps to obtain the simplified map

## Slide 4: Global Path Planning – A* Algorithm
Real size map
Reduced size map
Notes: Lukas 30 sec
Describe the reduction of the map
Describe the treatment of the path

## Slide 5: Filtering - Kalman
Standard Kalman Filter
Linearized model using first order approximation of sin and cos
Control input: speeds of the wheels
Measurement: position and angle seen by the camera
Two main functions
  state_prop: state propagation using the control input
  state_correct: state correction using the measurement
Notes: Lukas 20 sec
Describe the two main functions
Describe the control input and the measurement

## Slide 6: Motion Control
Path following
calculate distance to goal
if distance is above threshold:
calculate angle to goal
if angle is above threshold:
re-orient robot
else:
move robot
else:
increment goal index in path array
if index surpasses the length of the path:
stop the movement timer
Notes: Matthias 20 sec
Describe the normal motion control

## Slide 7: Local Obstacle Avoidance
Use of the proximity sensors at the front
Simple Neural Network controls the speeds (Exercise Week 3)
Priority over global path following
A distracted thymio driver is the local obstacle
Notes: Matthias 20 secs
Describe the obstacle avoidance motion control

## Slide 8: Conclusion
We implemented:
  Computer vision
  Global path planning
  Global path following
  State filtering
  Local obstacle avoidance
Possible improvements:
  Pathfinding algorithm returns a jagged path
  Obstacle avoidance is very basic
  Path following is very straight forward
  Offset on the position in the Kalman (camera perspective)
  A* does not work properly for extreme situations
Notes: JB 30 secs
Describe the possible improvements